## Slide 1: Drone Localization in Ad-hoc Indoor Environment
Marcell Rausch
2020.06.23

## Slide 2: Task
The student’s task is to develop a positioning system by placing stationary LIDAR sensors on a drone, to collect range measurements of its environment and use a SLAM algorithm to find the current position. The position and orientation of these sensors is fixed relative to the drone’s frame and scanning of the drone’s environment is done by orientation changes that happen due to the natural motion during flights.

## Slide 3: Motivation
Typically used sensors for mapping and localization
Planar scanners - LIDAR
  Accurate
  Too heavy for small vehicles
  Sensitive
  Expensive
Monocular, stereo or RGB-D camera
  Detailed maps
  Produces high amounts of data
  High computation needs

## Slide 4: VL53L1X LIDAR
4m maximum range
50Hz maximum sampling rage
Small size: 4.9x2.5x1.56mm
27° Field of view
Adjustable Region of Interest

## Slide 5: Google Cartographer SLAM
Inputs: LIDAR scan and IMU
2D and 3D online SLAM
Used by Google street view
Great community
Available as ROS package

## Slide 6: System design overview

## Slide 7: VL53L1X measurements
Sensor settings
Distance preset: Short, Medium, Long
Timing budget: 18.5ms, 33ms, 140ms, 200ms
Resolution by moving RoI: 1x1, 2x2, 3x3, 4x4

## Slide 8: VL53L1X simulation
1. Data collection
  Gazebo Simulator using ROS
  Iris drone using PX4 Repository
  360° LIDAR data
  Recorded into Rosbag
2. Data filtering
  Python script
  Converts raw LIDAR data to simulate VL53L1X sensors
    FoV, update rate, max distance
    Layout

## Slide 9: VL53L1X simulation
1. Data collection
  Gazebo Simulator using ROS
  Iris drone using PX4 Repository
  360° LIDAR data
  Recorded into Rosbag
2. Data filtering
  Python script
  Converts raw LIDAR data to simulate VL53L1X sensors
    FoV, update rate, max distance
    Layout

## Slide 10: Cartographer tuning
*Illustration
Complex process
Requires good understanding of parameters
Each setup requires different tuning

## Slide 11: SLAM setup evaluation
1.Visual inspection of produced map
Submap quality and reliability
Global map quality and reliability
2. RMS error calculation of SLAM trajectory
Against ground truth trajectory
Objective measure

## Slide 12: 2D SLAM Results
13 LIDARs to cover the 360° horizontal plane
Introduced sensor parameters one by one
  4x4 and 3x3 resolution has similar performance
  33ms timing budget and Long preset
  Maximum distance is crucial
Reduced the number of sensors until map building is reliable
  8 sensors proved to be the lowest number that is able to produce reliable maps
13 sensors
8 sensors

## Slide 13: 3D SLAM Results
43 LIDARs to cover the drone’s surroundings in 3D
Introduced sensor parameters one by one
The introduction of the last parameter maximum distance made the map building unreliable
3D SLAM is not reliable with 43 sensors so it is safe to assume it will not work with less
4x4, 33ms, 4m
4x4, 33ms,
2.75m

## Slide 14: Summary & Future work
Summary
2D SLAM works reliably using 8 sensors
  Requires tuning in different scenarios
  Maximum indoor distance 2.75m
3D SLAM is unreliable even with 43 sensors
  Still possible by using 2D SLAM and combine it with height information from another source
Future work
Velodyne Velabit LIDAR

## Slide 15: Bíráló kérdései
A drón maximális sebességét említette a kivonatban, azonban a dolgozatban nem tért ki rá részletesen, hogy miért 5 km/h lehet a maximuma, ami még nem befolyásolja nagyon negatívan a lokalizáció pontosságát?
Ön szerint a LIDAR es kamera szenzorok kombinációjával javítható lenne a pontosság?
Ön szerint milyen hatása lenne, ha a szenzor adatokat egy vezetéknélküli hálózaton kellene valós időben átküldeni, ahol pl. csomagvesztés és késleltetésingadozás léphet fel?

## Slide 16: Thank you for your attention!